# Integers
An integer type variable is a variable that can only hold whole numbers (eg. -2, -1, 0, 1, 2). C++ actually has four different integer variables available for use: char, short, int, and long. The only difference between these different integer types is that they have varying sizes — the larger integers can hold bigger numbers.
- a char is 1 byte
- a short is 2 bytes
- an int is either 2 or 4 bytes
- a long is 4 bytes

Size/Type	Range
1 byte signed	-128 to 127
1 byte unsigned	0 to 255
2 byte signed	-32,768 to 32,767
2 byte unsigned	0 to 65,535
4 byte signed	-2,147,483,648 to 2,147,483,647
4 byte unsigned	0 to 4,294,967,296
8 byte signed	-9,223,372,036,854,775,807 to 9,223,372,036,854,775,807
8 byte unsigned	0 to 18,446,744,073,709,551,615

# Float
The floating part of the name floating point refers to the fact that a floating point number can have a variable number of decimal places. For example, 2.5 has 1 decimal place, whereas 0.1226 has 4 decimal places.

There are three different floating point data types: float, double, and long double. A float is usually 4 bytes and a double 8 bytes, but these are not strict requirements, so sizes may vary. Long doubles were added to the language after it’s release for architectures that support even larger floating point numbers. But typically, they are also 8 bytes, equivalent to a double. Floating point data types are always signed (can hold positive and negative values).

## Suffix of “f” on float value
25 //int / 25l //long / 25u //unsigned / 25.0 //double / 25.0f //float

template<class T> T min(T a, T b)
{
  return (a < b) ? a : b;
}
float x = min(3.0f, 2.0f); // will compile
x = min(3.0f, 2);   // compiler cannot deduce T type
x = min(3.0f, 2.0); // compiler cannot deduce T type
## precision

The precision of a floating point number is how many digits it can represent without information loss.
Variables of type float typically have a precision of about 7 significant digits. Variables of type double typically have a precision of about 16 significant digits. Variables of type double are named so because they offer approximately double the precision of a float.
When outputting floating point numbers, cout has a default precision of 6 — that is, it assumes all variables are only significant to 6 digits, and hence it will truncate anything after that.

cout << setprecision(16); // show 16 digits
## Scientific notation
Scientific notation is a useful shorthand for writing lengthy numbers in a concise manner. In scientific notation, a number has two parts: the significand, and a power of 10 called an exponent. The letter ‘e’ or ‘E’ is used to separate the two parts. Thus, a number such as 5e2 is equivalent to 5 * 10^2, or 500. The number 5e-2 is equivalent to 5 * 10^-2, or 0.05.

Name	Description	Size*	Range*
char	Character or small integer.	1byte	signed: -128 to 127 unsigned: 0 to 255
short int (short)	Short Integer.	2bytes	signed: -32768 to 32767 unsigned: 0 to 65535
int	Integer.	4bytes	signed: -2147483648 to 2147483647 unsigned: 0 to 4294967295
long int (long)	Long integer.	4bytes	signed: -2147483648 to 2147483647 unsigned: 0 to 4294967295
bool	Boolean value. It can take one of two values: true or false.	1byte	true or false
float	Floating point number.	4bytes	+/- 3.4e +/- 38 (~7 digits)
double	Double precision floating point number.	8bytes	+/- 1.7e +/- 308 (~15 digits)
long double	Long double precision floating point number.	8bytes	+/- 1.7e +/- 308 (~15 digits)
wchar_t	Wide character.	2 or 4 bytes	1 wide character

* The values of the columns Size and Range depend on the system the program is compiled for. The values shown above are those found on most 32-bit systems. But for other systems, the general specification is that int has the natural size suggested by the system architecture (one "word") and the four integer types char, short, int and long must each one be at least as large as the one preceding it, with char being always one byte in size. The same applies to the floating point types float, double and long double, where each one must provide at least as much precision as the preceding one.

# Max and Min values
Properties of integer types
- CHAR_BIT - size of the char type in bits (it is not necessarily 8 bits)
- SCHAR_MIN, SHRT_MIN, INT_MIN, LONG_MIN, LLONG_MIN(C99) - minimum possible value of signed integer types: signed char, signed short, signed int, signed long, signed long long
- SCHAR_MAX, SHRT_MAX, INT_MAX, LONG_MAX, LLONG_MAX(C99) - maximum possible value of signed integer types: signed char, signed short, signed int, signed long, signed long long
- UCHAR_MAX, USHRT_MAX, UINT_MAX, ULONG_MAX, ULLONG_MAX(C99) - maximum possible value of unsigned integer types: unsigned char, unsigned short, unsigned int, unsigned long, unsigned long long
- CHAR_MIN - minimum possible value of char
- CHAR_MAX - maximum possible value of char
- MB_LEN_MAX - maximum number of bytes in a multibyte character
Properties of floating-point types
#include <cfloat>
- FLT_MIN, DBL_MIN, LDBL_MIN - minimum value of float, double, long double respectively
- FLT_MAX, DBL_MAX, LDBL_MAX - maximum value of float, double, long double respectively
- FLT_ROUNDS - rounding mode for floating-point operations
- FLT_EVAL_METHOD - evaluation method of expressions involving different floating-point types (only available in C99)
- FLT_RADIX - radix of the exponent in the floating-point types
- FLT_DIG, DBL_DIG, LDBL_DIG - number of decimal digits that can be represented without losing precision by float, double, long double respectively
- FLT_EPSILON, DBL_EPSILON, LDBL_EPSILON - difference between 1.0 and the next representable value of float, double, long double respectively
- FLT_MANT_DIG, DBL_MANT_DIG, LDBL_MANT_DIG - number of FLT_RADIX-base digits in the floating-point mantissa for types float, double, long double respectively
- FLT_MIN_EXP, DBL_MIN_EXP, LDBL_MIN_EXP - minimum negative integer such that FLT_RADIX raised to a power one less than that number is a normalized float, double, long double respectively
- FLT_MIN_10_EXP, DBL_MIN_10_EXP, LDBL_MIN_10_EXP - minimum negative integer such that 10 raised to a power one less than that number is a normalized float, double, long double respectively
- FLT_MAX_EXP, DBL_MAX_EXP, LDBL_MAX_EXP - maximum positive integer such that FLT_RADIX raised to a power one more than that number is a normalized float, double, long double respectively
- FLT_MAX_10_EXP, DBL_MAX_10_EXP, LDBL_MAX_10_EXP - maximum positive integer such that 10 raised to a power one more than that number is a normalized float, double, long double respectively
- DECIMAL_DIG - minimum number of decimal digits needed to represent all the significant digits for long double.[4] The value is at least 10. (only available in C99)